## Slide 1: Using Dynamic Rupture Simulations to Improve Ground Motion Hazard Models for Normal Faults
Yair Franco, Daniel Trugman
SSA 2026

## Slide 2: Motivation
Hazard assessments are basis for earthquake preparation
Developed in part with ground motion models (GMMs)
GMMs depend largely on empirical ground motion records
[Petersen et al., 2023]

## Slide 3: Motivation
Ground motion data for large normal-faulting earthquakes is relatively scarce
  Particularly near-fault records
Could this be affecting hazard estimates in normal-faulting environments?
Chart: 
| Strike-slip | Reverse | Normal | Unknown
Mechanism distribution of NGA-West2 records (Ancheta et al., 2014) | 54 | 25 | 19 | 2

## Slide 4: Motivation
Normal fault hazard may not be as well constrained as for other mechanisms
Implications for areas where normal faulting is more common

## Slide 5: Motivation
Dynamic simulations: see physical effects on ground motion
Simulation data has been used for developing GMMs
  Kinematic – neglect some important dynamic effects
  Assumptions made on dip-slip mechanisms
(Donahue & Abrahamson, 2014)
(All simulations here are reverse-slip)
(Hanging wall term regression for dip-slip)
Notes: -hanging wall effects
-normal vs reverse dynamics

## Slide 6: Method
SeisSol: 3D dynamic rupture simulations
Scenarios adapted from SCEC TPV10 model
  Normal fault dipping 60°
Velocity data from simulation converted to RotD50
30 x 15 km fault
3x3 km nucleation patch
(Homogenous domain)

## Slide 7: Method
Scenarios tested:
  Changing fault dip (25°-75°)
  Reverse-slip mechanism
  Moving nucleation patch
  Adding a 1D velocity model

## Slide 8: Method
GMM comparison:
  Data obtained via OpenQuake
  Active Crustal models
    Used in 2023 National Seismic Hazard Model
  Ratio of average of models vs. SeisSol PGVs used for comparison

## Slide 9: Results — base case
Trend towards underprediction except at surface trace
Radiating areas of higher PGV

## Slide 10: Results — reverse-slip case
Stronger ground motions than normal-slip (expected)
Greater underpredictions near the surface trace
Similar trend towards overprediction elsewhere

## Slide 11: Results — shallower hypocenter
Max PGVs lower than base case
Underprediction more prevalent

## Slide 12: Results — changing dip
Stronger localized discrepancies in shallow dip (30°)
Notes: Hypocenter here would be x = 15 km*cos(30) = 13km so the blob is not at the hypocenter but a little further downdip from it

## Slide 13: Results — changing dip
Pattern changes with dip
Constructive interference at y = 0 (centered along strike) more apparent at steeper dips
Normal faults are more commonly in the 50-70° range

## Slide 14: Results — 1D velocity model
Vp = 5 km/s, Vs = 2.9 km/s in the top 5 km
Overprediction throughout entire area

## Slide 15: Results — physical effects
Multi-stage rupture effect in some scenarios
Possibly caused by differences in stress

## Slide 16: Results — physical effects
(O’Connell et al., 2007)
Near-surface ”unclamping effect” unique to normal-slip

## Slide 17: Results — physical effects
(1D velocity model)
(Base case)

## Slide 18: Conclusions
Rupture simulations show dynamic effects that affect ground motion
  Rupture speeds and breaks in propagation
Variability beyond GMM uncertainties in a lot of cases
Hazard estimates would benefit from richer dataset including dynamic rupture simulation results
GM records
GM prediction models
Simulations
Hazard estimates